## Slide 1: Communication Kit (Kit 3)
Communication Foundation Lessons (CFL)
(Lesson Ref: CFL02)
CFL14: Hybrid Relay (LoRa-IoT) Communication

## Slide 2: Communication Kit : Contents
Communication Kit Components
Communication Creative Board

## Slide 3: Kit 3 Communication Creative Board - Features
LoRa Module I/F
ESP32
OLED I/F
NRF24L01 Module I/F
RFID I/F
SD Card Module I/F
Rotary Encoder
Mini
Breadboard
Power
Connector
ON/OFF Switch
Input DC Jack
Free Connectors

## Slide 4: CFL14: Hybrid Relay (LoRa-IoT) Communication
Things Needed
4
LoRa Transmitter:
LoRa Receiver:

## Slide 5: CFL14: Hybrid Relay (LoRa-IoT) Communication
DHT11 | ESP32 Pin
VCC | 5V
GND | GND
Data | 33

## Slide 6: CFL14: Hybrid Relay (LoRa-IoT) Communication
LoRa
WiFi

## Slide 7: CFL14: Hybrid Relay (LoRa-IoT) Communication
setup()
• Start Serial communication
• Initialize DHT11 temperature sensor
• Configure LoRa pins and start LoRa at 433 MHz
• Print “LoRa Sender Ready”
loop()
• Read temperature from DHT11
• If sensor read fails → print error and retry
• Print temperature value to Serial Monitor
• Send the temperature value as a LoRa packet
• Wait 3 seconds before sending the next reading
setup()
• Connect ESP32 to WiFi network (STA mode)
• Start an HTTP server on port 80
• Create webpage handler to display LoRa temperature
• Initialize LoRa receiver at 433 MHz
• Print IP address and "LoRa Receiver Ready"
loop()
• Handle incoming web browser requests
• Check for LoRa packets
• If a LoRa packet arrives:
- Read the temperature string
- Convert to float and store in loraTemperature
- Print value on Serial Monitor
• Small delay to allow WiFi tasks to run properly
LoRa Temperature Receiver + WiFi Web Dashboard
LoRa Temperature Sender (DHT11 → LoRa TX)
Code for Lesson CFL14 (CFL14_Lora_DHT11_Sender.ino)
(CFL14_Lora_DHT11_Receiver_And_WiFi_Bridge.ino)
https://github.com/info-zas/zas-robotics-communications/blob/main/01_FoundationProjects/CFL14_Hybrid_IoT_LoRa_To_LoRa_WiFi/CFL14_Lora_DHT11_Sender/CFL14_Lora_DHT11_Sender.ino
https://github.com/info-zas/zas-robotics-communications/blob/main/01_FoundationProjects/CFL14_Hybrid_IoT_LoRa_To_LoRa_WiFi/CFL14_Lora_DHT11_Receiver_And_WiFi_Bridge/CFL14_Lora_DHT11_Receiver_And_WiFi_Bridge.ino