## Slide 1: Communication Kit (Kit 3)
Communication Foundation Lessons (CFL)
(Lesson Ref: CFL02)
CFL02: ESP32 Setup - OLED, Pot, Encoder & Buzzer

## Slide 2: Communication Kit : Contents
Communication Kit Components
Communication Creative Board

## Slide 3: Kit 3 Communication Creative Board - Features
LoRa Module I/F
ESP32
OLED I/F
NRF24L01 Module I/F
RFID I/F
SD Card Module I/F
Rotary Encoder
Mini
Breadboard
Power
Connector
ON/OFF Switch
Input DC Jack
Free Connectors

## Slide 4: CFL02 : ESP32 Setup - OLED, Pot, Encoder & Buzzer
Things Needed

## Slide 5
CFL02 : ESP32 Setup - OLED, Pot & Buzzer
setup()
• Configure pin 16 as OUTPUT for the buzzer
• Initialize I2C communication on pins 21 (SDA) and 22 (SCL)
• Initialize the OLED display (128x64) with I2C address 0x3C
• Set text size and color for OLED output
loop()
• Read analog value from potentiometer on pin 15 (range: 0–4095)
• Clear OLED and display the potentiometer reading
• If value is above 4000:
– Turn buzzer ON (pin 16 HIGH)
Else:
– Turn buzzer OFF (pin 16 LOW)
• Wait for 300 ms
Code for Lesson CFL02 (CFL02_Pot_OLED.ino):

## Slide 6: CFL02_a : ESP32 Setup - OLED, Rotary Encoder & Buzzer
setup()
• Configure pin 16 as OUTPUT for the buzzer
• Configure rotary encoder pins:
– SW (33) as INPUT_PULLUP
– CLK (26) as INPUT
– DT (27) as INPUT
• Initialize I2C communication on pins 21 (SDA) and 22 (SCL)
• Initialize the OLED display (128x64) with I2C address 0x3C
• Display startup message on OLED
loop()
• Check rotary encoder button (SW):
– If pressed, turn buzzer ON briefly, then OFF
• Read encoder CLK state to detect rotation
• If rotation detected:
– If clockwise:
* Increase encoder count
* Turn buzzer ON briefly
– If counter-clockwise:
* Decrease encoder count
• Clear OLED and display current encoder count
• Small delay for debounce
6
Code for Lesson CFL02 (CFL02_RotaryEncoder_OLED.ino):