## Slide 1: Communication Kit (Kit 3)
Communication Foundation Lessons (CFL)
(Lesson Ref: CFL02)
CFL09: Half-Duplex Wireless Communication Using NRF24L01

## Slide 2: Communication Kit : Contents
Communication Kit Components
Communication Creative Board

## Slide 3: Kit 3 Communication Creative Board - Features
LoRa Module I/F
ESP32
OLED I/F
NRF24L01 Module I/F
RFID I/F
SD Card Module I/F
Rotary Encoder
Mini
Breadboard
Power
Connector
ON/OFF Switch
Input DC Jack
Free Connectors

## Slide 4: CFL09 : Half-Duplex Wireless Communication Using NRF24L01
Things Needed
4
ESP32-A:
ESP32-B:

## Slide 5: CFL09 : What is Simplex and Duplex Communication?
Communication in electronics can be:
  Simplex: One-way
    Definition: Data flows in only one direction
    Example:
    ESP32-A sends sensor data
    ESP32-B only receives
    Real-world analogy: TV broadcast
  Duplex: Two-way (Half or Full)
    Definition: Data flows in both directions
    Types:
    Half-Duplex: One direction at a time (walkie-talkie)
    Full-Duplex: Both directions at the same time (phone call)
  In Microcontrollers: Usually implement Half-Duplex

## Slide 6: CFL09 : Half-Duplex Communication Using NRF24L01
NRF24L01 allows duplex communication using:
  radio.stopListening(); to send
  radio.startListening(); to receive
You alternate between sending and receiving (Half-Duplex)
  Example Flow:
  ESP32-A sends data
  ESP32-B receives it
  ESP32-B replies
  ESP32-A receives reply

## Slide 7: CFL09 : Half-Duplex Communication Using NRF24L01
ESP32-A:
Potentiometer controls a value (e.g., "speed" or "brightness")
When pushbutton (pin 25) is pressed:
  Sends a message: "Pot: 3780, Enc: 12"
  Receiver ESP32-B turns LED ON if pot > 3000
ESP32-B:
Receives data
Displays Pot and Enc values on OLED
If pot > 3000:
  Turns ON LED and buzzer
Then sends back confirmation message: "Received, LED ON“
ESP32-A:
Receives the confirmation
Displays ACK on OLED

## Slide 8
  CFL09 : Half-Duplex Wireless Communication Using NRF24L01
NRF Transmitter
NRF Receiver

## Slide 9: CFL09 : Half-Duplex Wireless Communication Using NRF24L01

## Slide 10: CFL09 : Half-Duplex Wireless Communication Using NRF24L01
NRF24L01 – Transmitter & Receiver Workflow
1. Setup Transmitter & Receiver
Configure ESP32 + NRF24L01 on SPI pins
Connect OLED display for feedback
Set matching radio address for TX/RX
2. NRF24 Communication Workflow
Transmitter Side (TX)
ESP32 reads potentiometer value
Formats message as: "PotValue:XXXX"
Sends packet using NRF24L01 @ 2.4 GHz (32-byte payload)
OLED shows: “Sent: XXXX”
Uses SPI pins (CE, CSN, SCK, MOSI, MISO)
NRF24 Wireless Link
Short-range, high-speed 2.4 GHz radio link
Ideal for robot-to-robot, remote sensors, wireless controllers
Low power, reliable packet system with auto-acknowledge
Supports multiple nodes via unique radio addresses
Receiver Side (RX)
ESP32 detects packets using radio.available()
Reads data with radio.read()
Extracts potentiometer value from received message
OLED displays: “Recv: XXXX”
Github Link for Code:
(1). https://github.com/info-zas/Training/tree/main/GPREC/03_Communications/01_Code/03_Comm_Kit_NRF24L01_Transmitter_Encoder_Value
(2). https://github.com/info-zas/Training/tree/main/GPREC/03_Communications/01_Code/04_Comm_Kit_NRF24L01_Receiver_Encoder_Value